Homebrew Radio Design Deep Dive
01 - Introduction to Series

---
Deep Dive into Radios
- Look into the pieces that make up radios
  - Attempt to better understand each block that makes up a radio
- Focus on Amateur Radio - HF band
  - 2-30 MHz
- Focus on receiver first, then transmitter
  - Some pieces can do double duty
- Expect this video series to take time
  - Start high level, then low level, then mid level

---
Nod to other YouTube Creators
- Some great creators who focus on homebrew radios
  - Alan W2AEW – deep dives
  - Charlie Morris ZL2CTW– from first principles – component selection
  - Pete Juliano N6QW – great results, lacks details of the pieces
  - SolderSmoke N2CQR – MythBusters series is really good
- Take a slightly different path
  - Choose to use off the shelf kits for pieces where available
    - Save time, costs the same or less, longer wait for stuff to come
  - Build what needs to be built, some things will be cheaper

---
Most Basic Operation Level
- Receiver
  - In from Antenna
  - Out to a speaker
- Transmitter
  - Microphone or Morse key in
  - Out to an antenna

---
Typical Receiver Block Diagram

---
Receiver Pieces – Broad Strokes
- Amplifiers
  - Radio signals are very low level and need amplification
  - RF, IF, Audio
- Mixers
  - Shift signs up/down in frequency
- Oscillators
  - Tuners, drive mixer
- Filters
  - Filter out RF signals we don’t want - Bandpass

---
Technique
- Use off the shelf blocks
  - Build all blocks with SMA connector
  - Test each block
- Connect blocks together using SMA cables
  - Test blocks in combination
- Easy to swap out blocks
  - Comparison between alternates

---
Radio Design Deep Dive
02 - RF Test Equipment

---
Test Equipment
- Recent seismic shift in affordability of test equipment
  - NanoVNA - < $60
  - TinySA - < $60
  - 8 digit frequency counter - < $20
  - Total cost < $200 – would have been 10’ to 100’s of $K
- Build vs Buy pieces?
  - Crystal Tester
  - RF Noise Generator – less necessary but easy to build
- Do you really need these? Probably

---
NanoVNA
- Vector Network Analyzer
- Scans from 0.1-900 MHz
  - Does not do audio range – can’t scan audio filters
  - This series looks at RF (1-30 MHz range)
- Use NanoVNA to
  - Sweep filters (bandpass for receivers, lowpass for transmitters)
  - Sweep Antennas – check resonance
  - Sweep IF/RF Amplifiers
    - Make sure to use attenuators before/after the amplifier (power gain stages)

---
tinySA
- Spectrum Analyzer
- 50KHz to 350 MHz
  - Use for RF range 1-30 MHz
- Measure
  - Signal levels in dBm (dB into 50 Ohms)
  - Spectral purity/harmonics
- Make sure to use attenuators
  - Don’t blow up front end

---
YouTube Creators
- They have pro gear (typically HP) but have videos on less expensive NanoVNA and tinySA
- IMSAIGuy
  - Very good videos on using the NanoVNA and tinySA - Playlists
  - His Intro to Spectrum Analyzers video is a good place to start
- W2AEW
  - Very good videos on NanoVNA - Playlist

---
Attenuators
- Largely passive devices
- Reduce power levels for measurement
- Reduce power levels between radio block
  - Ex: VFO puts out too much power for mixer LO input
- Use appropriate power attenuators
  - Radio Transmitters can put out a lot of Watts
  - Spectrum Analyzers can’t take high power
  - Attenuator has to dissipate the extra power/heat

---
Attenuators
- Buy vs Build?
- Buy triple attenuator
- Buy adjustable attenuator
- Buy higher power attenuator
- Build individual small attenuators
  - Simple PCB design
  - Use between stages Ex: LO to mixer use 6 dB attenuator
  - Buy 1% precision SMT resistors
- All have SMA in/outs

---
Triple Attenuator Card
- Inexpensive
- Fixed 0, 10, 20, 30 dB values
  - 0 dB for passthru calibration?
- Not 1% resistors
- Relatively large/bulky
- Slow from overseas
- Easy quick front end scaling into
  tinySA and NanoVNA

---
Adjustable Attenuator
- Inexpensive - PE4302
- Adjustable 0-31.5 dB
  - Nice for small adjustment steps
- Limited input power
- Arduino designs out there – overkill?
- Switch board - binary coded
- Not purely passive – needs DC power supply
- Build into project box

---
Homebrew Attenuators (1)
- Attenuators lend themselves easily to homebrew construction
  - Can do while waiting on attenuators to arrive in the mail
  - Can also do “odd” values
  - Use on-line calculators for values
  - Manhattan style
  - Carbon composition resistors
  - Parallel junkbox 5% resistors
    - Higher power
    - Better precision – can get to 1%

---
Homebrew Attenuators (2)
- Small PCB
  - 1206 resistors
  - SMA male/female
  - Light enough to hang off port

---
Attenuators
- Always use Attenuators when measuring stages with power gain
  - Even “small signal” RF Amplifiers can blow up the NanoVNA and tinySA front end
  - Ex: 0 dBm from NanoVNA amplified by 20 dB ampliier = 20 dBm into tinySA – too much power
- Null out attenuators
  - TinySA set external gain to show “true” value with gain stages
- Where to put attenuators in measurement?
  - Sometimes on input of gain stage
    - Bear in mind output compression
  - Sometimes on output of gain stage
    - Protect

---
DC Block
- TinySA and NanoVNA should not have DC signals applied
- Capacitively couples input to output

---
8 Digit Frequency Counter
- Very cheap
- VCXO for stability and accuracy
- Accuracy adjustment pot
  - “Man with one clock...”
  - Can zero beat a VFO with WWV then use the VFO to adjust pot
  - Or, input from GPS programmed for 10 MHz output on PPS pin

---
Crystal Tester
- Used for hand selecting crystals used in Crystal Bandpass Filters
- Colpitts oscillator
- Manhattan construction
- Junkbox parts
- Use with 8 digit frequency counter for precision
- Bin crystals and hand select close crystals

---
Noise Generator
- Buy or build
  - NanoVNA has a sweep generator
- Low level output
- Use?
  - Receiver input simulus
  - Sweep using as source for tinySA?
- Measure output levels using tinySA

---
Radio Design Deep Dive
03 - RF Amplifiers

---
Kits and Parts RF Amplifier
- Kits and Parts - $12 for kit, $4 for PCB
  - 1 toroid transformer to wind
- 1/8W resistor pad spacing
- Large 1206? SMD caps

---
K&P RF Amp
- Spec: 22+ dBm power gain from 2-30 MHz
  - Measured +25-27 dBm gain - fairly flat response
  - +20 dBm gain up to 80 MHz
- 50 ohm input and 50 ohm output
- 100 milliwatt maximum output
- Measured power - 0.031A at 12V = 370mW

---
RF Amplifier - Schematic
- 12V power
- “Exotic” transistor 2SC5551A
  - 3 for $5 from K&P

---
RF Amplifier - NanoVNA Measurements
- Use 30 dB attenuator when measuring performance with NanoVNA
  - Measure S11, S12
- Where to put attenuator?
  - Before or after amp?
  - NanoVNA puts out 1 dBm
  - Amp has 27 dB gain
  - Amp has max 100 mW output

---
RF Amplifier - S21 (Gain)
- Attenuator in the NanoVNA output
- Calibrate NanoVNA with just attenuator
- Measured 26 dB gain
- Flat from 1MHz-30MHz

---
RF Amplifier - S21 (Gain)
- Measured from 1-100MHz
- +26 dB gain across HF band
- Still decent gain at higher frequencies
  - +20dBm @ 80 Mhz

---
RF Amplifier - VSWR
- About 1:1.5 across entire HF band
- If measured with attenuator before Amp it would measure 1:1

---
RF Amplifier - Uses
- Where to best place RF Amplification?
  - Between Antenna and Bandpass filter?
  - Between Bandpass filter and Mixer?
  - Between Mixer and Crystal Filter?
  - After Crystal Filter?
  - May need a few of these – Built 4

---
Radio Design Deep Dive
04 - AF Amplifiers

---
AF Amplifier
- Buy (EBay) or Build?
- Lots of choices here
  - LM386, LM380, LM384
- How much power?
- How much gain?
- Include pre-Amp for impedance matching?
- Test finger first by putting finger on input and listening for hum

---
LM386 Audio Amplifier
- 700 mW output power
- Wide Supply Voltage Range: 4 V–12 V or 5 V–18 V (-4 part)
- Low Quiescent Current Drain: 4 mA
- Voltage Gains from 20 to 200
- Ground-Referenced Input
- Self-Centering Output Quiescent Voltage
- High input impedance: 50kΩ
  - Want 50Ω input to match Mixer (Product Detector) 50Ω output

---
LM384 Audio Amplifier
- 5W audio output
- Wide supply voltage range: 12- to 26-V
- Voltage Gain Fixed at 50
- High input impedance: 150kΩ
  - Want 50Ω input to match Mixer (Product Detector) 50Ω output

---
LM380 Audio Amplifier
- 2.5W audio output
- Wide supply voltage range: 10V-22V
- Low quiescent power drain: 0.13W (VS= 18V)
- Voltage gain fixed at 50 (34 dB)
- High peak current capability: 1.3A
- Short circuit proof output
- High input impedance: 150kΩ
  - Want 50Ω input to match Mixer (Product Detector) 50Ω output

---
Audio Pre-Amplifier
- Use to match input impedance to the output impedance of the Product detector
- Not much gain needed here
- Charlie Morris ZL2CTM did design
- NE5534 pre-amplifier

---
Radio Design Deep Dive
05 - RF Mixers

---
Mixers
- Three port devices
  - LO – Local Oscillator in
  - RF – In/out connection
  - IF – In/out connection
- Technologies include
  - Diode Ring Mixers
- Transformer coupled
- Input drive level

---
Radio Design Deep Dive
06 - Oscillators

---
Radio Design Deep Dive
07 - Band Pass Filters

---
Radio Design Deep Dive
08 - Crystal Filters